## Slide 1: The Frequency Domain
Sinusoidal tidal waves
Copy of Katsushika Hokusai The Great Wave off Kanagawa at http://commons.wikimedia.org/wiki/File:The_Great_Wave_off_Kanagawa.jpg

## Slide 2: Domains
Images can be represented in different domains
  Spatial domain – the strength of light at points in space
  Frequency domain – the strength of patterns within an image
Frequency domain is useful for
  Image analysis
  Image compression
  Efficient processing

## Slide 3: Frequency Domain
Various frequency domains
  Discrete Cosine – used in image analysis and compression
  Fourier – used in image analysis and processing
  Wavelet – used in image analysis and compression
  Haar and others …
Each domain defines a set of patterns from which all images can be composed
The DCT and DFT domains use sinusoidal patterns

## Slide 4: Sinusoids
A sinusoidal is characterized by the amplitude, frequency, and phase

## Slide 5: Functions into sinusoids
Any function can be represented as the sum of sinusoids
Consider a one dimensional ‘square wave’.
Can it be represented as the sum of ‘non-square waves’?

## Slide 6: Decomposing functions into sinusoids
Start with a sin wave of the same frequency as the square wave. This is the “base” or “fundamental” frequency.

## Slide 7: Decomposing functions into sinusoids
Add a 3rd “harmonic” to the fundamental frequency. The amplitude is less than that of the base and the frequency is 3 times that of the base.

## Slide 8: Decomposing functions into sinusoids
Add a 5th “harmonic” to the fundamental frequency. The amplitude is less than that of the base and the frequency is 5 times that of the base.

## Slide 9: Decomposing functions into sinusoids
Add a 7th and 9th“harmonic” to the fundamental frequency.

## Slide 10: Decomposing functions into sinusoids
Adding all harmonics up to the 100th.

## Slide 11: Sinusoids (1D)
Consider the following sinusoidal function
f can be understood as a row profile
Amplitude is determined by A
Phase (shift) is given by phi
Frequency is controlled by u
  if u = 1 there is one cycle spanning the image
  U can be understood as the ‘number of cycles per image width’

## Slide 12: Sinusoids (1D) as images

## Slide 13: Discrete sinusoid
Take the continuous sinusoidal function into the discrete domain via sampling at ½ unit intervals.
One effect is to place an upper limit on the frequencies that can be captured via sampling.
U must be less than N/2 in order to be recoverable by the discrete samples. This is the Shannon-Nyquist limit.
Higher frequencies generate aliases

## Slide 14: Aliasing example
Consider a sinusoid such that u=1 over a span of 8 units.
Consider a sinusoid such that u=7 over a span of 8 units.
The resulting samples are identical. The two different signals are indistinguishable after sampling and hence are aliases for each other.

## Slide 15: Frequency Domain
The central idea in frequency domain representation is to
  Find a set of orthogonal sinusoidal patterns that can be combined to form any image
  Any image can be expressed as the weighted sum of these basis images.
  The DFT and DCT are ways of decomposing an image into the sum of sinusoidal basis images

## Slide 16: How to determine the amplitudes?
The DCT and DFT transformations are ways of decomposing a spatial image into sinusoidal basis images.
  The forward DCT goes from spatial to frequency. The inverse DCT goes from frequency to spatial.
  The DCT and DFT are invertible – no loss of information either way

## Slide 17: Notional conventions